## Slide 1: Computer Architecture 1
Computer Organization and Design T H E H A R D W A R E / S O F T W A R E I N T E R F A C E
[Adapted from Computer Organization and Design, RISC-V Edition, Patterson & Hennessy, © 2018, MK] [Adapted from Great ideas in Computer Architecture (CS 61C) lecture slides, Garcia and Nikolíc, © 2020, UC Berkeley]

## Slide 2: RV32 So Far…
Add/sub
add rd, rs1, rs2 sub rd, rs1, rs2
Add immediate
addi rd, rs1, imm
Load/store
lw lb
lbu rd,
sw rs1, rs2, imm
sb rs1, rs2, imm
Branching
beq rs1, rs2, Label
bne rs1, rs2, Label
bge rs1, rs2, Label
blt rs1, rs2, Label
bgeu rs1, rs2, Label
bltu rs1, rs2, Label
j Label

## Slide 3: RISC-V Logical Instructions
Useful to operate on fields of bits within a word
  e.g., characters within a word (8 bits)
Operations to pack /unpack bits into words
Called logical operations
Logical operations | C operators | Java operators | RISC-V instructions
Bit-by-bit AND | & | & | and
Bit-by-bit OR | ¦ | ¦ | or
Bit-by-bit XOR | ^ | ^ | xor
Shift left logical | << | << | sll
Shift right logical | >> | >> | srl

## Slide 4: RISC-V Logical Instructions
Always two variants
  Register: and x5, x6, x7 # x5 = x6 & x7
  Immediate: andi x5, x6, 3 # x5 = x6 & 3
Used for ‘masks’
  andi with 0000 00FFhex isolates the least significant byte
  andi with FF00 0000hex isolates the most significant byte
There is no logical NOT in RISC-V
  Use xor with 11111111two
  Remember - simplicity…

## Slide 5: Logical Shifting
Shift Left Logical (sll) and immediate (slli):
  slli x11,x12,2 #x11=x12<<2
  Store in x11 the value from x12 shifted by 2 bits to the left (they fall off end), inserting 0’s on right; << in C.
  Before: 0000 0002hex
  0000 0000 0000 0000 0000 0000 0000 0010two
  After: 0000 0008hex
  0000 0000 0000 0000 0000 0000 0000 1000two
What arithmetic effect does shift left have?
Shift Right: srl is opposite shift; >>

## Slide 6: Arithmetic Shifting
Shift right arithmetic (sra, srai) moves n bits to the right (insert high-order sign bit into empty bits)
For example, if register x10 contained
1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If execute srai x10, x10, 4, result is:
1111 1111 1111 1111 1111 1111 1111 1110two= -2ten
Unfortunately, this is NOT same as dividing by 2n
  Fails for odd negative numbers
  C arithmetic semantics is that division should round towards 0

## Slide 7: Assembler to Machine Code (More Later in Course)
foo.S
bar.S
Assembler
Assembler
foo.o
bar.o
Linker
a.out
Pre-built object file libraries
Machine code executable file
Assembler source files (text)
Assembler converts human- readable assembly code to instruction bit patterns
Machine code object files
lib.o

## Slide 8: How Program is Stored
Memory
Bytes
Program
One RISC-V Instruction = 32 bits
Data
RISC-V (63)

## Slide 9: Program Execution
Instruction is fetched from memory, then control unit executes instruction using datapath and memory system, and updates PC
(default add +4 bytes to PC, to move to next sequential instruction; branches, jumps alter)
Control
Datapath
Program Counter (PC)
Registers
Arithmetic-Logic Unit (ALU)
Processor
Read Instruction
Instruction Address
Memory |  |  |  |  | 
 | Program |  |  |  | 
 |  | Bytes |  |  | 
 | Data |  |  |  | 
PC (program counter) is a register internal to the processor that holds byte address of next instruction to be executed

## Slide 10: Helpful RISC-V Assembler Features
Symbolic register names
  E.g., a0-a7 for argument registers (x10-x17) for function calls
  E.g., zero for x0
Pseudo-instructions
= addi rd, rs, 0
Shorthand syntax for common assembly idioms
E.g.,
E.g.,
E.g.,
mv rd, rs li rd, 13 = nop =
addi rd, x0, 13 addi x0, x0, 0

## Slide 11: RISC V Function calls
main() int | { i,j,k,m; | 
... |  | What information mus
i = | mult(j,k); | ... compiler/programmer
m = | mult(i,i); | ... keep track of?
/* really dumb mult function */
int mult (int mcand, int mlier){ int product = 0;
while (mlier > 0) {
product = product + mcand; mlier = mlier -1; }
return product;
}
What instructions can accomplish this?

## Slide 12: Six Fundamental Steps in Calling a Function
Put arguments in a place where function can access them
Transfer control to function
Acquire (local) storage resources needed for function
Perform desired task of the function
Put return value in a place where calling code can access it and restore any registers you used; release local storage
Return control to point of origin, since a function can be called from several points in a program

## Slide 13: RISC-V Function Call Conventions
Registers faster than memory, so use them
a0–a7 (x10-x17): eight argument registers to pass parameters and two return values (a0-a1)
ra: one return address register to return to the point of origin (x1)
Also s0-s1 (x8-x9) and s2-s11 (x18-x27): saved registers (more about those later)

## Slide 14: Instruction Support for Functions (1/4)
... sum(a,b);... /* a,b:s0,s1 */
}
int sum(int x, int y) { return x+y;
}
address (shown in decimal) 1000
1004
1008
1012
1016
… 2000
C
RISC-V
In RISC-V, all instructions are 4 bytes, and stored in memory just like data. So, here we show the addresses of where the programs are stored.
2004

## Slide 15: Instruction Support for Functions (2/4)
... sum(a,b);... /* a,b:s0,s1 */
}
int sum(int x, int y) { return x+y;
}
address (shown in decimal) 1000 mv a0,s0
1004 mv a1,s1
1008 addi ra,zero,1016
sum
# x = a # y = b #ra=1016
#jump to sum # next inst.
1012 j
1016 …
…
2000 sum: add a0,a0,a1
2004 jr ra #new instr.“jump reg”
RISC-V
C

## Slide 16: Instruction Support for Functions (3/4)
C
RISC-V
... sum(a,b);... /* a,b:s0,s1 */
}
int sum(int x, int y) { return x+y;
}
Question: Why use jr here? Why not use j?
Answer: sum might be called by many places, so we can’t return to a fixed place. The calling proc to sum must be able to say “return here” somehow.
…
2000 sum: add a0,a0,a1
2004 jr ra #new instr.“jump reg”

## Slide 17: Instruction Support for Functions (4/4)
Single instruction to jump and save return address: jump and link (jal)
Before:
# ra=1016
# goto sum
1008 addi ra,zero,1016
1012 j sum
After:
1008 jal sum # ra=1012,goto sum
Why have a jal?
  Make the common case fast: function calls very common
  Reduce program size
  Don’t have to know where code is in memory with jal!

## Slide 18: RISC-V Function Call Instructions
Invoke function: jump and link instruction (jal) (really should be laj “link and jump”)
  “link” means form an address or link that points to calling site to allow function to return to proper address
  Jumps to address and simultaneously saves the address of the following instruction in register ra
jal FunctionLabel
Return from function: jump register instruction (jr)
  Unconditional jump to address specified in register: jr ra
  Assembler shorthand: ret = jr ra

## Slide 19: Summary of Instruction Support
Actually, only two instructions:
jal | rd, | Label – jump-and-link
jalr | rd, | rs, imm – jump-and-link register
j, jr and ret are pseudoinstructions!
j: jal x0, Label

## Slide 20: RISC-V Instruction Representation
High Level Language Program (e.g., C)
Assembly Language Program (e.g., RISC-V)
Machine Language Program (RISC-V)
Assembler
Hardware Architecture Description (e.g., block diagrams)
Logic Circuit Description (Circuit Schematic Diagrams)
lw lw sw sw
x3, 0(x10)
x4, 4(x10)
x4, 0(x10)
x3, 4(x10)
Out = AB+CD
A B
C D
IMEM
+4
DMEM
Branch Comp.
Reg []
Addr
DataW
DataR
0
2
0
pc
0
1
inst[11:7] AddrD
inst[19:15] AddrA DataA inst[24:20] AddrB DataB
inst[31:7] Imm.
Gen
pc+4
alu
mem
1
wb
alu 1
pc+4
1
Reg[rs1] ALU
0
pc
imm[31:0]
Reg[rs2]
wb DataD
Anything can be represented
as a number, i.e., data or instructions

## Slide 21: Instructions as Numbers (1/2)
Most data we work with is in words (32-bit chunks):
  Each register is a word
  lw and sw both access memory one word at a time
So how do we represent instructions?
  Remember: Computer only understands 1s and 0s, so assembler string “add x10,x11,x0” is meaningless to hardware
  RISC-V seeks simplicity: since data is in words, make instructions be fixed-size 32-bit words also
    Same 32-bit instructions used for RV32, RV64, RV128

## Slide 22: Instructions as Numbers (2/2)
One word is 32 bits, so divide instruction word into “fields”
Each field tells processor something about instruction
We could define different fields for each instruction, but RISC-V seeks simplicity, so define six basic types of instruction formats:
  R-format for register-register arithmetic operations
  I-format for register-immediate arithmetic operations and loads
  S-format for stores
  B-format for branches (minor variant of S-format)
  U-format for 20-bit upper immediate instructions
  J-format for jumps (minor variant of U-format)

## Slide 23: R-Format Instruction Layout
Number of bits in field
32-bit instruction word divided into six fields of varying numbers of bits each: 7+5+5+3+5+7 = 32
Examples
  opcode is a 7-bit field that lives in bits 6-0 of the instruction
  rs2 is a 5-bit field that lives in bits 24-20 of the instruction
7
5
5 3
Name of field
31
25 24
20 19
1514
12 11
Field’s bit positions
76
5 7
0
funct7 | rs2 | rs1 | funct3 | rd | opcode

## Slide 24: R-Format Instructions opcode/funct Fields
opcode: partially specifies what instruction it is
Note: This field is equal to 0110011two for all R-Format register-register arithmetic instructions
funct7+funct3: combined with opcode, these two fields describe what operation to perform
Question: You have been professing simplicity, so why aren’t opcode and funct7 and funct3 a single 17- bit field?
  We’ll answer this later
7
31 25 24 20 19 1514 12 11 76
7 5 5 3 5
0
funct7 | rs2 | rs1 | funct3 | rd | opcode

## Slide 25: R-Format Instructions Register Specifiers
7 5 5 3 5 7
rs1 (Source Register #1): specifies register containing first operand
rs2 : specifies second register operand
rd (Destination Register): specifies register which will receive result of computation
Each register field holds a 5-bit unsigned integer (0-31) corresponding to a register number (x0-x31)
31
25 24
20 19
15 14
12 11
7 6
0
funct7 | rs2 | rs1 | funct3 | rd | opcode

## Slide 26: R-Format Example
RISC-V Assembly Instruction:
add x18,x19,x10
Reg-Reg OP
add rd=18
add
rs2=10
rs1=19
7
5
5
3
7
5
31
25 24
20 19
1514
12 11
76
0
funct7 | rs2 | rs1 | funct3 | rd | opcode
7
5
5
3
7
5
31
25 24
20 19
1514
12 11
76
0
0000000 | 01010 | 10011 | 000 | 10010 | 0110011

## Slide 27: Your Turn
What is correct encoding of add x4, x3, x2 ? 1) 4021 8233hex 2) 0021 82b3hex 3) 4021 82b3hex 4) 0021 8233hex 5) 0021 8234hex 31 2524 2019 15 14 12 11 7 6 0 |  |  |  |  |  | 
0000000 | rs2 | rs1 | 000 | rd | 0110011 | add
0100000 | rs2 | rs1 | 000 | rd | 0110011 | sub
0000000 | rs2 | rs1 | 100 | rd | 0110011 | xor
0000000 | rs2 | rs1 | 110 | rd | 0110011 | or
 |  |  |  |  |  | and

## Slide 28: All RV32 R-format Instructions
0000000 | rs2 | rs1 | 000 | rd | 0110011 | add
0100000 | rs2 | rs1 | 000 | rd | 0110011 | sub
0000000 | rs2 | rs1 | 001 | rd | 0110011 | sll
0000000 | rs2 | rs1 | 010 | rd | 0110011 slt | 
0000000 | rs2 | rs1 | 011 | rd | 0110011 | sltu
0000000 | rs2 | rs1 | 100 | rd | 0110011 | xor
0000000 | rs2 | rs1 | 101 | rd | 0110011 | srl
0100000 | rs2 | rs1 | 101 | rd | 0110011 | sra
0000000 | rs2 | rs1 | 110 | rd | 0110011 | or
0000000 | rs2 | rs1 | 111 | rd | 0110011 | and
Different encoding in funct7 + funct3 selects different operations Can you spot two new instructions?

## Slide 29: I-Format Instructions
What about instructions with immediates?
  Compare:
    add rd, rs1, rs2
    addi rd, rs1, imm
  5-bit field only represents numbers up to the value 31: immediates may be much larger than this
  Ideally, RISC-V would have only one instruction format (for simplicity): unfortunately, we need to compromise
Define new instruction format that is mostly consistent with R-format
  Notice if instruction has immediate, then uses at most 2 registers (one source, one destination)

## Slide 30: I-Format Instruction Layout
Only one field is different from R-format, rs2 and funct7 replaced by 12-bit signed immediate, imm[11:0]
Remaining fields (rs1, funct3, rd, opcode) same as before
imm[11:0] can hold values in range [-2048ten , +2047ten]
Immediate is always sign-extended to 32-bits before use in an arithmetic operation
We’ll later see how to handle immediates > 12 bits
31
0
imm[11:0] | rs1 | funct3 | rd | opcode
25 24 20 19 15 14 12 11 7 6
12 5 3 5 7

## Slide 31: I-Format Example
0010011
OP-Imm
01111
rd=15
111111001110 00001 000
imm=-50 rs1=1 add
7
5
12 11
76
0
imm[11:0] | rs1 | funct3 | rd | opcode
RISC-V Assembly Instruction:
addi x15,x1,-50
31 20 19 1514
12 5 3

## Slide 32: All RV32 I-format Arithmetic Instructions
“Shift-by-immediate” instructions only use lower 5 bits of the immediate value for shift amount (can only shift by 0-31 bit positions)
One of the higher-order immediate bits is used to distinguish “shift right logical” (SRLI) from “shift right arithmetic” (SRAI)
imm[11:0] |  | rs1 | 000 | rd | 0010011 | addi
imm[11:0] |  | rs1 | 010 | rd | 0010011 | slti
imm[11:0] |  | rs1 | 011 | rd | 0010011 | sltiu
imm[11:0] |  | rs1 | 100 | rd | 0010011 | xori
imm[11:0] |  | rs1 | 110 | rd | 0010011 | ori
imm[11:0] |  | rs1 | 111 | rd | 0010011 | andi
0000000 | shamt | rs1 | 001 | rd | 0010011 | slli
0000000 | shamt | rs1 | 101 | rd | 0010011 | srli
0100000 | shamt | rs1 | 101 | rd | 0010011 | srai

## Slide 33: Xác định mã máy (Hệ hex) cho các lệnh sau
add x1, x2, x3 : 0x003100B3
addi x8, x6, -10: 0xFF630413
ori x7, x10, 0x04: 0x00456393
slli x5, x12, 2: 0x00261293
0000 000 | 0 0011 | 0001 0 | 000 | 0000 1 | 011 0011 | add
1111 1111 0110 |  | 0011 0 | 000 | 0100 0 | 001 0011 | addi
0000 0000 0100 |  | 0101 0 | 110 | 0011 1 | 001 0011 | ori
0000 000 | 0 0010 | 0110 0 | 001 | 0010 1 | 001 0011 | slli

## Slide 34: Load Instructions are also I-Type
The 12-bit signed immediate is added to the base address in register rs1 to form the memory address
  This is very similar to the add-immediate operation but used to create address not to create final result
The value loaded from memory is stored in register rd
5
base
3
width
7
LOAD
5
dest
31 20 19 1514
12 11
76
0
imm[11:0] | rs1 | funct3 | rd | opcode
12
offset[11:0]

## Slide 35: I-Format Load Example
000000001000
00010
010
01110 0000011
LOAD
imm=+8
rs1=2 lw rd=14 (load word)
5
base
7
LOAD
3 5
width dest
RISC-V Assembly Instruction:
lw x14, 8(x2)
31 20 19 1514
12 11
76
0
imm[11:0] | rs1 | funct3 | rd | opcode
12
offset[11:0]

## Slide 36: All RV32 Load Instructions
lbu is “load unsigned byte”
lh is “load halfword”, which loads 16 bits (2 bytes) and sign- extends to fill destination 32-bit register
lhu is “load unsigned halfword”, which zero-extends 16 bits to fill destination 32-bit register
There is no ‘lwu’ in RV32, because there is no sign/zero extension needed when copying 32 bits from a memory location into a 32- bit register
funct3 field encodes size and
‘signedness’ of load data
imm[11:0] | rs1 | 000 | rd | 0000011 | lb
imm[11:0] | rs1 | 001 | rd | 0000011 | lh
imm[11:0] | rs1 | 010 | rd | 0000011 | lw
imm[11:0] | rs1 | 100 | rd | 0000011 | lbu
imm[11:0] | rs1 | 101 | rd | 0000011 | lhu

## Slide 37: S-Format Used for Stores
Store needs to read two registers, rs1 for base memory address, and rs2 for data to be stored, as well immediate offset!
Can’t have both rs2 and immediate in same place as other instructions!
Note that stores don’t write a value to the register file, no rd!
RISC-V design decision is to move low 5 bits of immediate to where rd field was in other instructions – keep rs1/rs2 fields in same place
  Register names more critical than immediate bits in hardware design
20 19
1514
0
Imm[11:5] | rs2 | rs1 | funct3 | imm[4:0] | opcode
31 25 24
7
offset[11:5]
5
base
3
width
5
src
7
STORE
12 11 76
5
offset[4:0]

## Slide 38: S-Format Example
RISC-V Assembly Instruction:
sw x14, 8(x2)
0000000 01110
00010
010
01000 0100011
STORE
offset[4:0]
=8
SW
offset[11:5]
=0
rs2=14
rs1=2
combined 12-bit offset = 8
0000000
01000
20 19 1514
0
Imm[11:5] | rs2 | rs1 | funct3 | imm[4:0] | opcode
31 25 24
7
offset[11:5]
5 5
src base
7
STORE
12 11 76
3 5
width offset[4:0]

## Slide 39: All RV32 Store Instructions
Store byte, halfword, word
sb sh sw
Imm[11:5] |  | rs2 |  |  | rs1 |  |  | 000 |  |  | imm[4:0] | 0100011
Imm[11:5] |  | rs2 |  |  | rs1 |  |  | 001 |  |  | imm[4:0] | 0100011
Imm[11:5] |  | rs2 |  |  | rs1 |  |  | 010 |  |  | imm[4:0] | 0100011
width

## Slide 40: RISC-V Conditional Branches
E.g., beq x1, x2, Label
Branches read two registers but don’t write to a register (similar to stores)
How to encode label, i.e., where to branch to?

## Slide 41: Branching Instruction Usage
Branches typically used for loops (if-else,
while, for)
  Loops are generally small (< 50 instructions)
  Function calls and unconditional jumps handled with jump instructions (J-Format)
Recall: Instructions stored in a localized area of memory (Code/Text)
  Largest branch distance limited by size of code
  Address of current instruction stored in the program counter (PC)

## Slide 42: PC-Relative Addressing
PC-Relative Addressing: Use the immediate field as a two’s-complement offset to PC
Branches generally change the PC by a small amount
Can specify ± 211 ‘unit’ addresses from the PC
(We will see in a bit that we can encode 12-bit offsets as immediates)
Why not use byte as a unit of offset from PC?
  Because instructions are 32-bits (4-bytes)
  We don’t branch into middle of instruction

## Slide 43: Scaling Branch Offset
One idea: To improve the reach of a single branch instruction, multiply the offset by four bytes before adding to PC
This would allow one branch instruction to reach ± 211 × 32-bit instructions either side of PC
  Four times greater reach than using byte offset

## Slide 44: Branch Calculation
If we don’t take the branch:
PC = PC + 4 (i.e., next instruction)
If we do take the branch:
PC = PC + immediate*4
Observations:
  immediate is number of instructions to jump (remember, specifies words) either forward (+) or backwards (–)

## Slide 45: RISC-V Feature, n×16-bit Instructions
Extensions to RISC-V base ISA support 16-bit compressed instructions and also variable-length instructions that are multiples of 16-bits in length
To enable this, RISC-V scales the branch offset by 2 bytes even when there are no 16-bit instructions
Reduces branch reach by half and means that ½ of possible targets will be errors on RISC-V processors that only support 32-bit instructions (as used in this class)
RISC-V conditional branches can only reach ± 210
× 32-bit instructions on either side of PC

## Slide 46: RISC-V B-Format for Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate imm[12:1]
But now immediate represents values
-4096 to +4094 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)

## Slide 47: Branch Example, Determine Offset
RISC-V Code:
Loop: beq x19,x10,End
add x18,x18,x10
addi x19,x19,-1
j Loop
1
2
3
End: # target instruction 4
Branch offset =
4×32-bit instructions = 16 bytes
(Branch with offset of 0, branches to itself)
Count instructions from branch

## Slide 48: Branch Example, Determine Offset
1100011
BRANCH
?????
imm
000
BEQ
???????
imm
01010
rs2=10
10011
rs1=19
RISC-V Code:
Loop: beq x19,x10,End
add x18,x18,x10
addi x19,x19,-1
j Loop
End:
1
2
3
# target instruction 4
Count instructions from branch

## Slide 49: Branch Example, Determine Offset
1100011
BRANCH
000
BEQ
???????
imm
01010
rs2=10
10011
rs1=19
RISC-V Code:
Loop: beq x19,x10,End
add x18,x18,x10
addi x19,x19,-1
j Loop
End:
1
2
3
# target instruction 4
Offset = 16 bytes
= 8 x 2
01000
?????
imm

## Slide 50: RISC-V Immediate Encoding
Only bit 7 of instruction changes role in immediate between S and B
Upper bits sign-extended from inst[31] always
31
Instruction encodings, inst[31:0]
25 24 20 19 15 14 12 11
0
funct7 | rs2 | rs1 | funct3 | rd | opcode
31
1
25 24
32-bit immediates produced, imm[31:0]
12 11 10 5 4
0
30
8 7 6
imm[11:0] |  | rs1 | funct3 | rd | opcode
imm[11:5] | rs2 | rs1 | funct3 | imm[4:0] | opcode
imm[12¦10:5] | rs2 | rs1 | funct3 | imm[4:1¦11] | opcode
R-type I-type S-type B-type
-inst[31]- | inst[30:25] | inst[24:21] | inst[20]
-inst[31]- | inst[30:25] | inst[11:8] | inst[7]
I-imm.
S-imm.
B-imm.
-inst[31]- | inst[7] | inst[30:25] | inst[11:8] | 0

## Slide 51: Branch Example, Complete Encoding
0000000010000
000 1000 0 1100011
BEQ imm[4:1] BRANCH
beq x19,x10, offset = 16 bytes
13-bit immediate, imm[12:0], with value 16
imm[0] discarded,
always zero
imm[11]
imm[12]
0 000000 01010 10011
imm[10:5] rs2=10 rs1=19

## Slide 52: All RISC-V Branch Instructions
beq bne blt bge bltu bgeu
imm[12¦10:5] | rs2 |  | rs1 | 000 |  | imm[4:1¦11] | 1100011
imm[12¦10:5] | rs2 |  | rs1 | 001 |  | imm[4:1¦11] | 1100011
imm[12¦10:5] | rs2 |  | rs1 | 100 |  | imm[4:1¦11] | 1100011
imm[12¦10:5] | rs2 |  | rs1 | 101 |  | imm[4:1¦11] | 1100011
imm[12¦10:5] | rs2 |  | rs1 | 110 |  | imm[4:1¦11] | 1100011
imm[12¦10:5] | rs2 |  | rs1 | 111 |  | imm[4:1¦11] | 1100011

## Slide 53: Questions on PC-addressing
Does the value in branch immediate field change if we move the code?
  If moving individual lines of code, then yes
  If moving all of code, then no (‘position-independent code’)
What do we do if destination is > 210 instructions away from branch?
  Other instructions save us

## Slide 54: Questions on PC-addressing
Does the value in branch immediate field change if we move the code?
  If moving individual lines of code, then yes
  If moving all of code, then no (‘position-independent code’)
What do we do if destination is > 210 instructions away from branch?
Other instructions save us
beq x10,x0,far
# next instr 
bne x10,x0,next j far
next: # next instr

## Slide 55: U-Format for “Upper Immediate” Instructions
Has 20-bit immediate in upper 20 bits of 32-bit instruction word
One destination register, rd
Used for two instructions
  lui – Load Upper Immediate
  auipc – Add Upper Immediate to PC
31
0
imm[31:12] | rd | opcode
20
U-immediate[31:12] U-immediate[31:12]
12 11 7 6
5
dest dest
7
LUI AUIPC

## Slide 56: LUI to Create Long Immediates
LUI writes the upper 20 bits of the destination with the immediate value, and clears the lower 12 bits.
Together with an addi to set low 12 bits, can create any 32-bit value in a register using two instructions (lui/addi).
lui x10, 0x87654 | # | x10 = | 0x87654000
addi x10, x10, 0x321 | # | x10 = | 0x87654321

## Slide 57: One Corner Case
How to set 0xDEADBEEF?
lui x10, 0xDEADB # x10 = 0xDEADB000 addi x10, x10, 0xEEF # x10 = 0xDEADAEEF
addi12-bit immediate is always sign-extended, if top bit is set, will subtract -1 from upper 20 bits

## Slide 58: Solution
How to set 0xDEADBEEF?
LUI x10, 0xDEADC # x10 = 0xDEADC000
ADDI x10, x10, 0xEEF
# x10 = #0xDEADBEEF
Pre-increment value placed in upper 20 bits, if sign bit will be set on immediate in lower 12 bits.
Assembler pseudo-op handles all of this:
li x10, 0xDEADBEEF # Creates two
#instructions

## Slide 59: AUIPC
Adds upper immediate value to PC and places result in destination register
Used for PC-relative addressing
Label: AUIPC x10, 0 # Puts address of
# Label in x10

## Slide 60: J-Format for Jump Instructions
jal saves PC+4 in register rd (the return address)
  Assembler “j” jump is pseudo-instruction, uses JAL but sets
rd=x0 to discard return address
Set PC = PC + offset (PC-relative jump)
Target somewhere within ±219 locations, 2 bytes apart
  ±218 32-bit instructions
Immediate encoding optimized similarly to branch instruction to reduce hardware cost
7 6
0
12 11
5
dest
7
JAL
imm[20] | imm[10:1] | imm[11] | imm[19:12] | rd | opcode
1
10 1 8
offset[20:1]
31 30 21 20 19

## Slide 61: Uses of JAL
# j pseudo-instruction
j Label = jal x0, Label # Discard return address
instructions
# Call function within 218 of PC
jal ra, FuncName

## Slide 62: JALR Instruction (I-Format)
jalr rd, rs, immediate
  Writes PC+4 to rd (return address)
  Sets PC = rs + immediate
  Uses same immediates as arithmetic and loads
    no multiplication by 2 bytes
    In contrast to branches and jal
7 6
0
12 11
12
offset[11:0]
5
dest
7
JALR
imm[11:0] | rs1 | func3 | rd | opcode
31 20 19 15 14
5
base
3
0

## Slide 63: Uses of JALR
# ret and jr psuedo-instructions ret = jr ra = jalr x0, ra, 0
# Call function at any 32-bit absolute address
lui x1, <hi20bits> jalr ra, x1, <lo12bits>
# Jump PC-relative with 32-bit offset auipc x1, <hi20bits>
jalr x0, x1, <lo12bits>

## Slide 64: Summary of RISC-V Instruction Formats
31
0
funct7 | rs2 | rs1 | funct3 | rd | opcode
30
25 24 21 20 19 15 14 12 11 8 7 6
imm[11:0] |  | rs1 | funct3 | rd | opcode
imm[11:5] | rs2 | rs1 | funct3 | imm[4:0] | opcode
imm[12¦10:5] | rs2 | rs1 | funct3 im | m[4:1¦11] | opcode
imm[31:12] | rd | opcode
imm[20¦10:1¦11]] | imm[19:12] | rd | opcode
R-type I-type S-type B-type U-type
J-type

## Slide 65: Sử dụng lệnh jalr để triển khai switch
switch(expression) {
case constant-expression :
statement(s);
break; /* optional */
case constant-expression :
statement(s);
break; /* optional */
/* you can have any number of case statements */
default : /* Optional */
statement(s);
}

## Slide 67: Complete RV32I ISA
Open Reference Card ¨ |  |  |  |  |  |  | 
Base Integer Instructions: RV32I |  |  |  |  |  |  | 
Category Name | Fmt | RV32I Base |  |  |  |  | 
Shifts Shift Left Logical | R | SLL rd,rs1,rs2 |  |  |  |  | 
Shift Left Log. Imm. | I | SLLI rd,rs1,shamt |  |  |  |  | 
Shift Right Logical | R | SRL rd,rs1,rs2 |  |  |  |  | 
Shift Right Log. Imm. | I | SRLI rd,rs1,shamt |  |  |  |  | 
Shift Right Arithmetic | R | SRA rd,rs1,rs2 |  |  |  |  | 
Shift Right Arith. Imm. | I | SRAI rd,rs1,shamt |  |  |  |  | 
Arithmetic ADD | R | ADD rd,rs1,rs2 |  |  |  |  | 
ADD Immediate | I | ADDI rd,rs1,imm |  |  |  |  | 
SUBtract | R | SUB rd,rs1,rs2 |  |  |  |  | 
Load Upper Imm | U | LUI rd,imm |  |  |  |  | 
Add Upper Imm to PC | U | AUIPC rd,imm | Loads Load Byte | I | LB rd,rs1,imm |  | 
Logical XOR | R | XOR rd,rs1,rs2 | Load Halfword | I | LH rd,rs1,imm |  | 
XOR Immediate | I | XORI rd,rs1,imm | Load Byte Unsigned | I | LBU rd,rs1,imm |  | 
OR | R | OR rd,rs1,rs2 | Load Half Unsigned | I | LHU rd,rs1,imm |  | 
OR Immediate | I | ORI rd,rs1,imm | Load Word | I | LW rd,rs1,imm |  | 
AND | R | AND rd,rs1,rs2 | Stores Store Byte | S | SB rs1,rs2,imm |  | 
AND Immediate | I | ANDI rd,rs1,imm | Store Halfword | S | SH rs1,rs2,imm |  | 
Compare Set < | R | SLT rd,rs1,rs2 | Store Word | S | SW rs1,rs2,imm |  | 
Set < Immediate | I | SLTI rd,rs1,imm |  |  |  |  | 
Set < Unsigned | R | SLTU rd,rs1,rs2 |  |  |  |  | 
Set < Imm Unsigned | I | SLTIU rd,rs1,imm |  |  |  |  | 
Branches Branch = | B | BEQ rs1,rs2,imm | Synch Synch thread | I | FENCE Not | in 61C | 
Branch ≠ | B | BNE rs1,rs2,imm |  |  |  |  | 
Branch < | B | BLT rs1,rs2,imm | Environment CALL | I | ECALL |  | 
Branch ≥ | B | BGE rs1,rs2,imm | BREAK | I | EBREAK |  | 
Branch < Unsigned | B | BLTU rs1,rs2,imm |  |  |  |  | 
Branch ≥ Unsigned | B | BGEU rs1,rs2,imm |  |  |  |  | 
Jump & Link J&L | J | JAL rd,imm |  |  |  |  | 
Jump & Link Register | I | JALR rd,rs1,imm |  |  |  |  |